Title
The APEX Control System*
Past, Present & Future
APECS Developers: A. Belloche, H. Hafok, J. Hatchell, C. König, D. Muders,
E. Polehampton, R. Schaaf, F. Schuller, F. v.d.Tak, F. Wyrowski
* APECS

---
APECS’ Roots in ALMA
Early (1999/2000) contact to ALMA software development groups since APEX will be a copy of an ALMA prototype antenna
Worked in SSR & HLA groups
Later followed Test Interferometer Control Software (TICS) developments
Evaluated ALMA-TI FITS raw data format for use at APEX
Now still working for ALMA (DC, Heuristics)
1999-2000-2001-2002-2003-2004-2005-2006-2007

---
Lessons learned from ALMA Work
Interfaces must be stable early on
Object-oriented software analysis & design
Unified Modeling Language (UML) (A standardized way of translating requirements into a class and object structure)
Distributed computing using a middleware like CORBA (Common Object Request Broker Architecture)

---
Don’t panic ! I’m just an object.
Name: FLASH810
Properties: Frequency, Sideband
Methods: On, Tune, Off

---
Inherited ALMA Software
APECS re-uses a large portion of the original ALMA Test Facility (ATF) software
Advantages:
  - Common hardware & interfaces
  - Real-time software already developed
  - Big development team (->2003: 15, 2003->: 50)
  - Potential upgrades (and support) in the future
Disadvantages:
  - APEX is an early adopter. Steep learning curve.
  - Initial releases are typically unstable

---
ALMA Common Software
ACS (v1.1 & v2.0.1) provides:
  - CORBA
  - Distributed Objects (Container / Component model) to abstract hardware
  - Configuration database
  - Property value monitoring
  - Multi-language environment (C++, Python, Java)

---
CORBA
CORBA facilitates the communication among pieces of software in distributed, heterogeneous, multilanguage environments

---
Test Interferometer Control Software
TICS (v0.2, v0.5 & April 2004) provides:
  - Real-time software (VxWorks)
  - CAN (Controller Area Network) CORBA objects and bus interface to VERTEX ACU/PTC
  - Astronomical coordinate handling (descriptive RA/Dec and horizontal)
  - Basic patterns (linear, arc, curve strokes including On-The-Fly mode)
  - Monitoring database
  - Optical pointing

---
APECS Developments
ACS & TICS provide the basic infrastructure but a full telescope control system requires:
  - Hardware interfaces (“IDL”, “SCPI”)
  - Raw data format (“MBFITS”)
  - High-level observer interface (“apecs CLI”)
  - Observation coordination (“Observing Engine”)
  - Raw data writing (“FitsWriter”)
  - Online calibration pipeline (“Calibrator”)
  - Automatic observation logging (“Observation Logger”)
  - Monitoring tools (“Monitoring Engine”)

---
Hardware Interfaces
For each device one needs a CORBA Interface Definition Language (IDL) file
CORBA C++ code is complicated. Instead embedded APEX systems use a simple ASCII protocol based on SCPI* commands sent via UDP sockets
SCPI commands are derived from naming hierarchy and method and property names
C++ code is auto-generated from IDLs
*Standard Commands for Programmable Instrumentation

---
SCPI Syntax Example
Component sends the device:
[APEX:]<device name>:<property name>?
The device replies:
[APEX:]<device name>:<property name> <value> \
<ISO 8601 time stamp>
Example:
APEX:HET460:LO2:MULTI1:backShort2?
APEX:HET460:LO2:MULTI1:backShort2 2.341 \
2003-11-05T10:19:38.310+00.00

---
Generic Instrument Interfaces
APECS uses high-level interfaces that are designed to be generic, i.e. applicable to any instrument of a given class (e.g. heterodyne receivers or continuum backends)
The instrument setup thus needs to be implemented only once
Adding new instruments to the system is reduced to simply adding names

---
Multi-Beam FITS (MBFITS)
ALMA-TI FITS turned out to be unsuitable for the multi-beam single-dish data expected for APEX
Began extending ALMA-TI FITS together with IRAM 30m and Effelsberg with the goal to share (mainly calibration) software
Many detailed iteration cycles led to the MBFITS format which is now well iterated, stable and has been in use for 2 years

---
“apecs” Command Line Interface
IPython based CLI with extensible scripting language including user macros
High-level commands to set up:
  - Catalogs (source, line)
  - Targets (coordinates, velocity)
  - Instruments (frontends, backends)
  - Calibrations (sky-hot-cold, skydip, point, focus)
  - Switch modes (total power, wobbling, freq. sw.)
  - Patterns (single, raster, OTF, (spiral))

---
Observing Engine
Central coordinating process that sets up all devices according to the “Scan Objects” sent via the “apecs” CLI
Pattern loop to set up receivers, IF, backends, antenna motion and start / stop FitsWriter and backends
Background threads to update weather and IERS parameters needed for coordinate and refraction calculations

---
Observing Engine Interactions

---
FitsWriter
The FitsWriter creates MBFITS files by collecting telescope, backend and monitoring data via a set of pipelines
Each pipeline consists of pipes and filters and feeds a particular type of MBFITS binary table
A flexible mechanism allows to store any CORBA property at any given rate in the MONITOR table

---
Calibrator
The calibrator provides the online pipeline to process the MBFITS files after each subscan
Spectral line data is calibrated to TA* scale using ATM and written to CLASS format
Bolometer data is processed using the BoA modules
Pointing & focus results are made available to the “apecs” CLI for corrections

---
Observation Logger
Automatic creation of the observer’s log (XML & HTML) using the online information
Allows editing a comment field for each scan
Visible columns can be selected individually

---
Monitoring Engine
Generic graphical status display engine using the ACS archiving notification channel
Displays can be created using the standard “Qt Designer” program obeying a given naming convention for values, descriptions and units

---
APECS Key Facts
Modern object-oriented & distributed design
Generic instrument interfaces facilitate adding new devices
Automatic interface code generator
Simple ASCII communication to embedded systems
High-level scripting language
Generic GUIs
Monitoring database
Simulation system for developments (demo)

---
Future APECS Developments I
New observing patterns (spirals, circles, more complex lists of strokes)
Array de-rotation
Frequency switching mode
Wobbler mode

---
Future APECS Developments II
MBFITS split into several files using FITS hierarchical groups
Porting to ACS 5 under Scientific Linux 4.2
New servers for Chajnantor
“xapecs” GUI